## Slide 1: Team 3 – Healthy Body Vitamins
John Wittgen, William Shehane, Brian Waterson, Caine Wilson

## Slide 2: Project Objective
Design a new facility that effectively and efficiently integrates
material handling, storage, and product flow to meet the future
needs of Healthy Body Vitamins and includes manufacturing space for Vital Brand™.

## Slide 3: What is the problem?
HBV needs a new facility to host all their operations.
  It will include the following layout allocations:
      25,000ft2 Corporate Offices.
      4,000 ft2 Vital Brand Manufacturing.
      3000 ft2 HBV Outlet Store.
173,000 ft vs 215,000 ftfacility size.
12 vs 16 dock doors.
5 years of growth.
Parking and corporate offices.

## Slide 4: Projects Activities and tasks
Determine Supply and Demand for the company
1
Calculate required square footage for warehouse based off racks
2
Come up with design (Will require many itterations)
3
Create Arena Model
4
Cost Breakdown of Facility
5

## Slide 5: DMAIC Gantt Chart
Define:
Understand project assignment
Define the scope of the project
Gather initial assumptions
Understand the growth of demand
Develop Initial Facility Blueprint
Build the Project Charter
Measure:
Assign locations for facility departments
Analyze flows between departments
Convert given data for simulation use
Analyze:
Develop a process simulation
Change manufacturing variables and gather output
Improve:
Analyze simulation output change
Decide on most efficient manufacturing scenario regarding cost

## Slide 6: Supply and Demand Graphs
t
Click to add text
Line 2 Upgraded
New Line Added
Notes: Increase the size, condense the units, change the obsess and do not include the 6th year. Add indications of when the new line or upgrades are needed. Nice explanation to the question John. Add the upgrade of the second line to recommend to the year 5. All lines are upgraded by year 5

## Slide 7: Design Iteration 1
The original drawing given to the team was not to scale to 173,000 sqft accurately
The team scaled down the facility to keep the same facility shape.
The team needed this information to be accurate to ensure the warehousing space could accommodate as many storage racks as possible.
Scaling math can be found on the next page.

## Slide 8: Scaling Math
On the left are the calculations for the sizing of the layout of the facility.
Above are the calculations for the sizing of the departments within the facility.

## Slide 9: Design Iteration 3
Prior to meeting with the sponsor, the team was recommended that the facility needed accommodations for employees such as offices for the foreman, a breakroom, restrooms, a cafeteria, etc.
The team was not considering a ticketing department for the goods to be prices during the distribution process, so that department was added.
The team included a forward storage area to accommodate.

## Slide 10: Final Facility Design
The team decided to include the ticketing operation at the end of the process, so the department is places closest to the shipping department.
The facility was then sectioned into different warehousing locations to determine the distances between the departments to support with the Arena simulation.
The team also considered to split the shipping and receiving departments to help with routing and to further support the Arena simulation.

## Slide 11: Department Centroids
Include Calculations Here
Centroid calculations for department routes

## Slide 12: Routes
Receiving Routes:
R -> 1 = R –7-3-4-1
R -> 2 = R-7-3-4-5-2
R -> 3 = R-7-3
R-> 4 = R-7-3-4
R-> 5 = R-7-3-4-5
R-> 6 = R-7-6
R -> 7 = R-7
R-> 8 = R-7-8
R-> 9 = R-7-8-9
Manufacturing Routes:
M -> 1 = M-3-4-1
M -> 2 = M-3-4-5-2
M -> 3 = M-3
M -> 4 = M-3-4-5
M -> 5 = M-3-4-5
M -> 7 = M-3-7
M -> 8 = M-3-4-8
M -> 9 = M-3-4-5-9
Picking Routes:
1 -> S = 1-4-8-T-S
2-> S = 2-5-4-8-T-S
3-> S = 3-4-8-T-S
4-> S = 4-8-T-S
5-> S = 5-4-8-T-S
7 -> S = 7-8-T-S
8-> S = 8-7-T-S
9-> S = 9-8-T-S

## Slide 13: Distance Calculations
It was necessary to find this information on the amount of distance traveled between departments to calculate the time delays between departments with forklift travel times

## Slide 14: Arena Model Slide

## Slide 15: Arena Model Off Load

## Slide 16: Arena Model Production Details

## Slide 17: Arena Model Transport Details

## Slide 18: Arena Model Output
Arena Model Efficiency | 90% of Calculated | Calculated | 110% of Calculated | 125% Of Calculated
Avg Total Trucks Shipped | 7.48 | 6.8 | 6.12 | 5.1
Worker Utilization | 0.828 | 0.91 | 1.001 | 1.1375
Avg Transport Time | 118.25 sec | 131.39 sec | 144.53 sec | 1.64.24 sec

## Slide 19: Arena Model Shortcomings
Model starts from scratch each run.
Model utilizes an arrival distribution.
It doesn’t simulate overtime.
The simulation doesn’t deal with expiration.
Model required assumptions about storage time and employee efficiency.
  This could have been tested and examined if a more in-depth study was conducted.
  Model required shipment amount estimates.

## Slide 20: Equipment Cost Breakdown
Majority of equipment costs stem from initial manufacturing costs and line expenses

## Slide 21: Cost Breakdown: Manufacturing
Aside from production line costs, employee salaries and computer/software costs take up the majority of manufacturing costs
Another fluctuating cost variable to take into account is machine maintenance

## Slide 22: Cost Breakdown: Warehouse/Storage
Pallet racking system is the main warehousing cost with both two and three stack systems to be utilized
Dock leveling implemented at all 12 dock doors
Forklift cost listed with both charging and maintenance costs included

## Slide 23: Conclusions/Recommendations
173,000 sq ft facility
12 dock doors
Price ticketing in warehouse after manufacturing
Upgrade one of the lines to a high speed line after first year
Add a new high speed line after year three

## Slide 24: Future Study
More focus on employee specifics
How will items be stored
Some items need to be ticketed in facility and some in store
What type of equipment is going to be used
Wage increases and additional hiring over time

## Slide 25: Questions

## Slide 26: Appendix

## Slide 27: Design Iteration 2
The team decided locations for the outlet store, corporate offices, manufacturing spaces, and a separate storage area for the raw materials for manufacturing
The team also decided the layout of the lane within the warehouse to accommodate material handling equipment and racking systems

## Slide 28: Initial Assumptions
Assume 9ft wide dock door
Assume dock door height is the same as a trailer
Stacking limitation – 3 pallets high
Assumed delays between locations and operator timing given flows
Forklifts all move at the same constant speed
No use of AGVs
Assume internally generated funds are added, borrowed funds from the company have a 12% internal inflation rate
The area needed for a new production line also includes the amount of space needed for operators to work in as well
Max load of forklift exceeds the lifting requirements for finished goods and raw materials
No area needed for a shipping department
SKUs are handled with dual picking
Capital equipment can be stored in the lanes
Space for raw materials needed for equipment
No need for a maintenance department, all maintenance work is out-contracted
Totes fit onto full size pallets for Finished Goods and Shipping
Every forklift/ piece of capital is operated by one person
There is 4’ of space between doors
The addition on the north side of the building is a semicircle forming to the curved road

## Slide 29: Order of Objectives
Understand project assignment
Define the scope of the project
Gather initial assumptions
Understand the growth of demand
Develop Initial Facility Blueprint
Build the Project Charter
Assign locations for facility departments
Analyze flows between departments
Convert given data for simulation use
Develop a process simulation
Change manufacturing variables and gather output
Analyze simulation output change
Decide on most efficient manufacturing scenario regarding cost

## Slide 30: Overall Challenges/short comings
Arena
Everything is good on here